## Slide 1: Building Construction
A fire resistive rating (FRR) is given in minutes or hours and relates to how long it takes to burn through a given material.
Expressions like “2-hour fire resistive rating” or “2-hour fire wall” relate to the length of time it takes to burn through types of building materials.
Flame spread rating (FSR) is used with interior finishes.
The FSR denotes how long it takes to burn across the surface of something.

## Slide 2: Building Codes and Ratings
The building codes will stipulate the allowable building construction types, fire resistance ratings, and flame spread ratings
The allowable construction type of a building is directly related to the occupancy of the building, the area per floor, and/or the number of stories.

## Slide 3: Examples of Fire Rating Standards
ASTM E119 - 10a: Standard Test Methods for Fire Tests of Building Construction and Materials
  Example of testing procedures for determining the fire resistance ratings of construction materials
ANSI/UL 10B, Fire Tests of Door Assemblies
  Example of testing procedures for fire doors

## Slide 4: NFPA 220, Standard Types of Building Construction
NFPA 220 defines types of building construction based on the combustibility and the fire resistance rating of a building’s structural elements
  Note: Fire walls, nonbearing exterior walls, nonbearing interior partitions, fire barrier walls, shaft enclosures, and openings in walls, partitions, floors, and roofs are not related to the types of building construction and are regulated by other standards and codes, where appropriate.

## Slide 5: NFPA 220
Types of construction defined by the fire resistance rating (in hours) of the
Type I though Type V
  Type I, Fire Resistive: Consists of precast concrete slabs supported by precast columns and precast girders.
  Type II, Noncombustible: The weight bearers are generally steel beams and girders. (If the building is Type II (000), the beams and girders are all “unprotected” steel.)
  Type III, Ordinary: Can consist of a mix of materials, including wood and concrete.
  Type IV, Heavy Timber: Construction using heavy timber. To qualify as heavy timber, a wood member must meet a certain thickness requirement.
  Type V, Wood Frame: All-wood construction.

## Slide 6: Type of Construction and Fire Resistance Rating
  For example, Type I
    Can be Type I (442) or Type I (332)
  With Type I (442):
The three Arabic numerals in parentheses following the Roman numeral indicate the fire resistance of the exterior bearing walls, structural frame, and floor, respectively.

## Slide 7: NFPA 5000, Building Construction and Safety Code
Protects building occupants and contents with the latest requirements for construction, protection, and occupancy features needed to minimize danger to life and property
Provides complete rules for new construction, building rehab, and safety enforcement

## Slide 8: International Building Code
Developed by the International Code Council
  www.iccsafe.org
A large portion of the International Building Code deals with fire prevention
Many states and jurisdictions have adopted all or parts of the IBC.

## Slide 9: IBC and Pennsylvania
Statewide adoption of the following IBC Codes
  2006 International Building Code
  2006 International Energy Conservation Code
  2006 International Existing Building Code
  2006 International Fire Code
  2006 International Fuel Gas Code
  2006 International Mechanical Code
  2006 ICC Performance Code
  2006 International Plumbing Code
  2006 International Residential Code
  2006 International Urban Wildland Interface Code

## Slide 10: Wood
Pros and Cons?
Fire resistance
What does charring do to a wood structure?
Pros and cons of engineered trusses

## Slide 11: Masonry and Brick
Pros and Cons?
Fire resistance
How does heat affect masonry and brick construction?

## Slide 12: Steel
Pros and Cons?
Fire resistance
How does heat affect steel construction?
Does steel burn?

## Slide 13: Gypsum
Pros and Cons?
Fire resistance
If gypsum is fire resistant, what allows it to be resistant?

## Slide 14: Plastics
Pros and Cons of plastics in construction?
Fire resistance
What is Exterior Insulation Finishing System (EIFS)?

## Slide 15: Glass
Pros and Cons?
Fire resistance
How does heat affect glass?
What can be done to glass to improve its resistance?